## Slide 1: FIRST Robotics and the Design Process
Andrew Blatner with material from Team 1114 and Karthik Kanagasabapathy

## Slide 5: Identify the Problem
Clear solution-neutral problem statement
Example: A company has several acres of lawn that they must maintain. They ask a gardener what kind of lawnmower would be best.
What’s wrong with this?
Why a lawnmower? What about goats?
Better question: How can we best keep the grass short?

## Slide 6: Identify the Problem
Constraints: Limits on the design
  Weight, size, number of motors, battery type, cost, safety
Criteria: Requirements of the design
  Score basketballs, balance bridge, drive speed,

## Slide 7: Identify the Problem
In the 2012 FRC game:
  Rules said we could have opening in bumpers and single 14” extension
  We immediately jumped to roller intake through opening and 14” bridge mechanism
What’s wrong here?
Unnecessarily constrained the problem
Overlooked not going through bumpers, but over
Many teams combined intake and bridge mechanism into one

## Slide 8: Identify the Problem
Shooter: Focused on distance and accuracy
Problem: You didn’t get points for shooting far or accurately
  Points came from SCORING
Should have focused on how to best score
  Shoot straight at backboard with fast backspin

## Slide 9: Brainstorming
Collect as many ideas as possible
As individual, then as group
All ideas heard one at a time
NO criticism at this stage: kills creativity
Build off each other’s ideas
Should be relaxed, free atmosphere

## Slide 10: Brainstorming
Large number of ideas wanted
Out of the ordinary ideas wanted
Combine and improve ideas
Keep all ideas concise and short
  Shouldn’t have lengthy and detailed descriptions

## Slide 11: Conceptualization
Evaluating brainstormed ideas
Rough designs, sketches, outlines
  Do not write out every detail, dimension, etc.
Determining most plausible solutions
Important to visualize solutions

## Slide 12: Prototyping
Taking selected ideas to build and test functional models
Important to test for the right qualities and the right problem
  Why it’s critical to correctly identify the problem
2012 season
  We prototyped for accuracy and distance
  Not for scoring ability

## Slide 13: Iteration
Core!!! to the design process
Cyclic process of prototyping, testing, analyzing, and refining
Taking ideas and modifying them based on tests and new information

## Slide 21: Golden Rule #2
It’s better to have 3 excellent mechanisms than 5 mediocre ones
K.I.S.S – Keep It Super Simple (or Safe)
Excellent mechanisms take more resources, so you can’t have as many
  Will still make your robot better at what it does